Vehicular Networks
Alison Chaiken
alison@she-devel.com
Presented to the UCSC Extension course
“Networking Fundamentals"
Aug 9, 2021

---
List of vehicle-relevant networks
Vehicular Networks
Common in automated systems and robotics:
- Precision Timing Protocol (IEEE 1588), to sync clocks of hosts
- Time-Sensitive Networking (IEEE 802.1 and 1722), to prioritize critical messages
  - CAN or Internet payload
- CV2X and DSRC wireless (not 802.11)
- Controller Area Network

---
Renesas example network topology
Renesas Network for Modern Autos
entrance
facilities
external
gateways/firewalls
Each vehicle is an Autonomous System.

---
Motivation for vehicular subnetworking
Motivation: Vehicular Subnetworks
- Different bus speeds and cabling.
- Different security domains.
  - Problem: interconnection of various domains.
  - Example: driver displays with brake and music-player info.
- CAN gateways interconnect subnetworks.

---
OSI model of classic CAN
Courtesy Microchip

---
ECUs are CAN nodes
Courtesy Microchip
Sensor or actuator

---
CAN clock and bit stuffing
CAN Clock
From Understanding and Using the Controller Area Network Communication Protocol
Clock is derived from data “bit stuffing.”

---
MAC in CAN: CSMA/CR
Bus Arbitration: CSMA/Collision Resolution
From Understanding and Using the Controller Area Network Communication Protocol

---
CAN message format and transport
CAN Data Frame Basics
- 11- or 29-bit ID determined by “claiming” procedure.
- Messages are acknowledged (like WiFi).
- Protocol supports Remote Request and Error frames.
- Classic CAN: 8B MTU, up to 1 Mb/s.
- CAN FD: 64B MTU, up to 5 Mb/s.
- All messages are broadcast: connectionless.
- HW filters determine which messages an ECU (electronic control unit) processes.

---
CAN gateway routing
Renesas Gateway Routing: static packet filtering
AVB = audio-video bridging (IEEE 1722)
CAN IDs

---
Summary
Summary
- Like Ethernet and IP, is old but evergreen.
- Differs from TCP/IP at every protocol layer.
- CAN classic and CAN FD are PHY and Link Layer protos.
- High layers have many standards and vendors.
- Wide application in vehicles, robotics, industrial applications, agriculture . . .

---
Scripts for demo
#!/bin/bash
set -e
set -u
echo "****Existing networks before VCAN addition****"
ip link show
echo "***********************************************"
echo ""
# tell Linux about virtual CAN nodes: necessary one time
#sudo ip link add type vcan
sudo ip link add dev vcan0 type vcan
sudo ip link set up vcan0
echo "****Networks after VCAN addition****"
ip link show
echo "***********************************************"
echo ""
#!/bin/bash
set -e
set -u
count=$(ip link show | grep vcan | wc -l)
echo "Removing ${count} vcan devices"
echo ""
while (( --count > -1 )); do
  echo "removing vcan${count}"
  sudo ip link del dev vcan${count}
  echo ""
done
echo "****Removed vcan devices:****"
ip addr list
echo "***********************************************"
Then $ cangen -n 5 -m

---
railroad network
Example: railroad control system

---
Legacy automotive network
Older image of passenger vehicle network
Cameras and LIDARS:
TSN
TSN

---
railroad network and OSI model
CANopen and ISO-TP provide higher levels
Example: railroad gateway